## Slide 1
TEXTBOOK
Introductory Circuit Analysis, Boylestad, 12th Ed
Lecture 3
Attribution Nidhal Abdulaziz
ENGG104 Electrical Systems

## Slide 2: Lecture 2 summary
Energy and Power P = W/t
Series Circuit – current is the same in the branch
Adding voltage sources
Resistors in series – you add them
Kirchhoff's Voltage Law – all voltages add to zero around a complete loop.
Voltage divider rule – voltages divide proportionally to resistance
Real Voltage source – internal resistance reduces output voltage

## Slide 3: Lecture 3 Outline
Boylestad – Chapters (6,7 )
Parallel Circuits
Kirchhoff's Current Law (KCL) - all currents in and out of a node sum to zero.
Current Dividers – current splits in proportion to resistance

## Slide 4: Parallel Circuits
With parallel circuits, components share two common connections
  E.g. points A and B in the circuit shown opposite
With parallel circuits, all components experience the same voltage across them
  E.g. the voltage E in the circuit shown
  A good example of a parallel circuit is the house wiring system

## Slide 5: Example parallel circuits
FIG. 6.1 (a) Parallel resistors; (b) R1 and R2 are in parallel; (c) R3 is in parallel with the series combination of R1 and R2.
Node
Node
Node
Node

## Slide 6: More examples
Note all are the same circuit just drawn differently
FIG. 6.2 Schematic representations of three parallel resistors.

## Slide 8: Total Resistance
For resistors in parallel as shown in Fig. 6.3, the total resistance is determined from the following equation:
FIG. 6.3 Parallel combination of resistors.

## Slide 9: Rearranging the equation
The Total Resistance of parallel resistors is always less than the value of the smallest resistor

## Slide 10: Examples: What is the total resistance?
RT = RT =
FIG. 6.4 Parallel resistors for Example 6.1.
FIG. 6.5 Parallel resistors for Example 6.2.

## Slide 12: Example: What is the total resistance
RT =
FIG. 6.6 Network to be investigated in Example 6.3.

## Slide 14: Note: Redrawing circuit
Circuit from previous slide
FIG. 6.7 Network in Fig. 6.6 redrawn.

## Slide 15: Special cases: Two branches
Most of the time, we only have two branches in parallel
FIG. 6.4 Parallel resistors for Example 6.1.

## Slide 16: Special case: All resistors are equal
FIG. 6.9 Three equal parallel resistors to be investigated in Example 6.5.

## Slide 17: Measuring resistance
Remember always in parallel
FIG. 6.17 Using an ohmmeter to measure the total resistance of a parallel network.

## Slide 18: Parallel Circuits
The Voltage across parallel elements is the same.
For Single Source Networks, The source current is equal to the sum of the individual branch currents.

## Slide 20: KIRCHHOFF’S CURRENT LAW
Kirchhoff’s current law (KCL):
  The algebraic sum of the currents entering and leaving a junction (or region) of a network is zero.
FIG. 6.31 (a) Demonstrating Kirchhoff ’s current law; (b) the water analogy for the junction in (a).

## Slide 21: KIRCHHOFF’S CURRENT LAW
I1 =
I3 =
I4 = I5 =
FIG. 6.33 Four-node configuration for Example 6.17.

## Slide 22: KIRCHHOFF’S CURRENT LAW
Note I1 + I2 = I3 rewriting I1+ I2 – I3 = 0 [KCL-sum of all currents in and out of node sum to zero]
At point b I3 – I4 + I5 = 0
Notice all currents entering a node are positive and all currents exiting node are negative.

## Slide 23: KCL example
I3 = I5=

## Slide 25: Another KCL example
Is =

## Slide 27: CURRENT DIVIDER RULE
  For two parallel elements of equal value, the current will divide equally.
  For parallel elements with different values, the smaller the resistance, the greater is the share of input current.
  For parallel elements of different values, the current will split with a ratio equal to the inverse of their resistance values.

## Slide 29: Current Divider example
Question: how will the 9 A split?
10 times more current in 10  resistor than in 100 resistor and 100 times more than 1000 resistor

## Slide 30: Current Divider Rule
Special Case: 2 resistors in parallel

## Slide 31: KCL example
Determine I1 and I2
Verify KCL

## Slide 32: Lecture 3 summary
Parallel Circuits
Kirchhoff's Current Law (KCL) - all currents in and out of a node sum to zero.
Current Dividers – current splits in proportion to resistance