## Slide 1
Boylestad and Nashelsky, Prentice Hall, 2006 , Ch 1
Semiconductors
PN Junctions
Ideal Diodes
Attribution Nidhal Abdulaziz
Lecture 13
Semiconductors, Diodes

## Slide 2: Semiconductors
A Semiconductor has a conductivity that is between a conductor and insulator
Most used single crystal semiconductor materials are Germanium (Ge), Silicon (Si) and compound structure semiconductor is Gallium Aresenide (GaAs)

## Slide 3: Semiconductors
Basic behaviour of a semiconductor can be explained using the atomic structure – note the number of valence electrons leading to covalent bonding between atoms making the atomic structure strong.
Copper (Cu) has 29 [2,8,8,8,3] electrons and Aluminium (Al) has 13 [2,8,3] electrons. The valence electrons can be dislodged easily making Al and Cu good conductors.
Boylestad and Nashelsky, page 3
We use the pure material of silicon, and then we add impurity from a different type of semiconductor material.
e.g. we add few atoms of gallium onto silicon to create a process called doping

## Slide 4: Semiconductors
The covalent bonding - sharing of the valence electrons makes the dislodgement of electrons more difficult
Boylestad and Nashelsky, page 3

## Slide 5: Semiconductors
By applying sufficient energy from external sources the covalent bond can be broken and the electrons can be released (reaching a free state)
External sources include light energy, thermal energy
Pure semiconductor materials (intrinsic materials) can be subjected to a doping process leading to an extrinsic material
By introducing an impurity material (Antimony, Arsenic, Phosphorous) with 5 valence electrons to Si an n – type semiconductor material is formed (leaving one free electron per atom –negative charge)
By introducing an impurity material (Boron, Gallium, Indium) with 3 valence electrons to Si a p – type semiconductor material is formed (leaving one hole per atom – positive charge)

## Slide 6: Semiconductors
n-type material
Boylestad and Nashelsky, pages 7, 8
p-type material

## Slide 7: Semiconductors
Boylestad and Nashelsky, pages 9
Electron vs Hole flow
When an electron moves a hole will be created
When the electron is moving from 1 hole to
Another, is it as if the hole is moving in the opposite direction.
When electron moves, it will leave a hole.
When the electron is moving to the left, the hole is moving to the right.
The hole does not move. It is the electron who is moving.

## Slide 8: Semiconductors
Boylestad and Nashelsky, page 9
In an n-type material majority carriers are electrons and the minority carries are holes
In a p-type material majority carriers are holes and the minority carries are electrons

## Slide 9: Semiconductor Diode
A key semiconductor component is the PN junction diode, formed by joining P and N type semiconductors (through a metallurgical process)
With no voltage (no bias) applied across the terminals a depletion region is created – electrons and the holes at the junction will combine developing a shortage of carriers
Boylestad and Nashelsky, page 9
Symbol of diode
No Free electrons (or holes) to conduct
cathode
anode
Electrons try to jump from right to left
Holes try to jump from left to right
All electrons and holes have stabilized with each other.
We don’t have free electrons or free holes to move. We call this the depletion region.

## Slide 10: Semiconductor Diode
With forward bias across the terminals a depletion shrinks in its width thus making the current conduction easier
Boylestad and Nashelsky, page 12
Electrons attracted to positive side of battery
Holes attracted to negative side of battery

## Slide 11: Semiconductor Diode
With reverse bias across the terminals a depletion is grown in its width thus making the current conduction more difficult
Boylestad ad Nashelsky, page 12
Electron will try to go to positive side of battery. Hence
The depletion region will increase
Depletion region becomes wider

## Slide 12: The ideal Diode
The ideal diode, only allows charge to flow in one direction.
  This is known as ‘Forward bias’
No current flows in the negative direction
  Known as ‘Reverse bias’
We can make use this diode characteristic to use the diode as a switch. When it is forward bias, the switch is on.
When it is reverse biased, the switch is off.

## Slide 13: The two states of a Diode

## Slide 14: A Diode Rectifier Circuit

## Slide 15: More Examples

## Slide 16: The Practical Diode
The practical diode v-I characteristics
Due to the potential drop that develops as a result of the depletion region about 0.7V of forward bias is required before current starts increasing when forward biased
A small leakage current does exist when reverse biased due to minority carriers
Boylestad and Nashelsky, page 14

## Slide 17: Semiconductor Diode
The practical vs ideal diode v-i characteristics
Boylestad and Nashelsky, page 21

## Slide 18: Diode Circuits
Given the (nominal) zero resistance of a conducting diode, a series resistor must always be included in diode circuits, as shown opposite
A Light Emitting Diode (LED) is a diode which emits light when passing current
  Common colours: red, green, yellow
  The light intensity is proportional to the diode current
The battery needs to be more than 0.7 V for
the diode to start conducting

## Slide 19: Practical Diode Continued
A Diode usually needs a 0.7V in the forward bias to get the current moving
If we keep increasing the voltage to a large number, there will be a breakdown.
The current will be very large in the opposite direction. Diode has been damaged. It is no longer a diode.
There is a continuous flow of current through the diode.

## Slide 20: Practical Diode Continued

## Slide 21
Wave-shaping Circuits
Necessary to shape waveforms
Many examples can be found in transmitters and receivers in TV or radar or equipment control and protection circuits
Uses diodes and zener diodes for clipping and clamping (shaping) input

## Slide 22: Rectifiers Overview
Half Wave rectifier
a. What is the use of the transformer?
To step down the voltage
220V -> 12 V

## Slide 23: Bridge Rectifier

## Slide 24: Current Flow in the Bridge Rectifier

## Slide 25: Current Flow in the Bridge Rectifier

## Slide 26: Bridge Rectifier, RC Filter
To improve the DC waveform that is generated at the output we use additional RC circuit.
The capacitor will charge and discharge.
We will choose time constant RC so that the capacitor cannot discharge quickly. It will take
A long time to discharge the capacitor, until the second halve will come and it will charge again.
We still have ripples at the output. We will use the regulator circuit to regulate the voltage at the output.

## Slide 27: Example: DC power supply circuit
220 V in UAE and Europe