## Slide 1
Lecture 4
Introductory Circuit Analysis, Boylestad, 12th Ed
Attribution Nidhal Abdulaziz
ENGG104 Electrical Systems

## Slide 2: Lecture 3 summary
Parallel Circuits
Kirchhoff's Current Law (KCL) - all currents in and out of a node sum to zero.
Current Dividers – current splits in proportion to resistance

## Slide 3: Lecture 4 Outline
Boylestad – Chapters (7 and 8 )
Series/Parallel Circuits
The current source
Current/voltage source conversion
Nodal analysis

## Slide 4: Series/Parallel Circuits
A series-parallel configuration is one that is formed by a combination of series and parallel elements.
FIG. 7.1 Series-parallel dc network.
Note: R3 in series
with R4. Together
They are in
Parallel with R2.
All of them are
In series with R1

## Slide 5: From the previous slide – Reduce and Return
R’=R3+R4 (series)
R’T=R2//R’ (parallel)
RT = R’T+R1
Now we can determine Is
Then use current divider
To determine branch currents
Or Voltage divider

## Slide 6: Example 1
Determine I3
FIG. 7.3 Series-parallel network for Example 7.1.
Hint: only use voltage divider without
Determining source current.

## Slide 8: Example 2
Determine I4, V2 and Is in this order

## Slide 10: Another example
Determine currents

## Slide 12: Typical exam question
Determine the unknowns

## Slide 13: Challenge 1
Much easier than you think 
FIG. 7.22 Example 7.8.

## Slide 14: Current Sources
Although current sources are available as laboratory supplies, they appear extensively in the modeling of electronic devices such as the transistor.
Just as a battery provides a fixed voltage to a network, a current source establishes a fixed current in the branch where it is located.
FIG. 8.1 Introducing the current source symbol.

## Slide 15: Current Sources
In general, a current source determines the direction and magnitude of the current in the branch where it is located.
Furthermore, the magnitude and the polarity of the voltage across a current source are each a function of the network to which the voltage is applied.

## Slide 16: Example
Current I1 will always be 10 mA in the branch where the current source is
V1 = 10mA x 20K = 200V
(Ohms law V=IR)
What’s Vs?
FIG. 8.2 Circuit for Example 8.1.

## Slide 17: Source Conversion
FIG. 8.6 Source conversion.

## Slide 18: Source Conversion Example
What’s IL in both circuits? What is the VL in both circuits?

## Slide 19: Source Conversion Example
Convert 4 A current source to the voltage source then redraw and solve.

## Slide 20: Current Sources in Parallel
We found that voltage sources of different terminal voltages cannot be placed in parallel because of a violation of Kirchhoff’s voltage law.
  Similarly, current sources of different values cannot be placed in series due to a violation of Kirchhoff’s current law.

## Slide 21: Current Sources in Parallel
However, current sources can be placed in parallel just as voltage sources can be placed in series.
  In general, two or more current sources in parallel can be replaced by a single current source having a magnitude determined by the difference of the sum of the currents in one direction and the sum in the opposite direction. The new parallel internal resistance is the total resistance of the resulting parallel resistive elements.

## Slide 22: Example
KCL at top node 6A – 10A = -4A (4A heading down)
Total resistance

## Slide 23: Example 1

## Slide 24: Example 2

## Slide 25: Current Sources Can NOT be connected in Series
current sources of different current ratings are not connected in series, just as voltage sources of different voltage ratings are not connected in parallel.

## Slide 26: Nodal Analysis
We now turn our attention to nodal analysis—a method that provides the nodal voltages of a network, that is, the voltage from the various nodes (junction points) of the network to ground.
The method is developed through the use of Kirchhoff’s current law in much the same manner as Kirchhoff’s voltage law was used to develop the mesh analysis approach.

## Slide 27: Nodal Analysis Method
Determine the number of nodes within the network.
Pick a reference node, and label each remaining node with a subscripted value of voltage: V1, V2, and so on.
Label current directions and polarities.
Apply Kirchhoff’s current law at each node except the reference.
Solve the resulting equations for the nodal voltages.

## Slide 28: Nodal Analysis by Example
Step 1 and 2: Label the nodes (2 nodes in this case, V1 and ground 0V)

## Slide 29: Example
Step 3: Label current direction and polarities
Step 4: Apply KCL at node V1 1A = I1+I2
(or -I1-I2+1 = 0 in general terms)
I1 is just the current through R1=> use ohms law
I2 is the current through R2 => use ohms law
Substitute back into KCL equation

## Slide 30: Example with 2 nodes to solve

## Slide 31: Ctd...
Apply steps 1 and 2 and 3
Step 4: Write KCL at node 1 and KCL on Node 2
Step 1 and 2 Label nodes
Step 3 directions and polarities

## Slide 32: Ctd...
solving

## Slide 33: Remember Cramer’s rule
...Or use any equation solver

## Slide 34: Another Example
V1 =
V2 =

## Slide 36: One last example

## Slide 38: Lecture 4 summary
Series/Parallel Circuits
The current source
Current/voltage source conversion
Nodal analysis