## Slide 1
Introductory Circuit Analysis, Boylestad, 12th Ed
Lecture 9 - 10
ENGG104 Electrical Systems

## Slide 2
Chapter 14 – Boylestad
Sinusoidal response of resistor, inductor and capacitor
Low and high frequency response of inductors and capacitors
Average power and Power Factor
Basic Elements and Phasors

## Slide 3: 13.7 – Average Value
Understanding the average value using a sand analogy:
  The average height of the sand is that height obtained if the distance form one end to the other is maintained while the sand is leveled off.
Notes: 20

## Slide 4: Average Value
The algebraic sum of the areas must be determined, since some area contributions will be from below the horizontal axis.
  Area above the axis is assigned a positive sign and area below the axis is assigned a negative sign.
The average value of any current or voltage is the value indicated on a dc meter – over a complete cycle the average value is the equivalent dc value.
Notes: 21

## Slide 5: Example 5

## Slide 6: Example 5 solution

## Slide 7: Example 6

## Slide 8: 13.8 – Effective (rms) Values
How is it possible for a sinusoidal ac quantity to deliver a net power if, over a full cycle the net current in any one direction is zero (average value = 0).
Irrespective of direction, current of any magnitude through a resistor will deliver power to that resistor – during the positive and negative portions of a sinusoidal ac current, power is being delivered at each instant of time to the resistor.
The net power flow will equal twice that delivered by either the positive or the negative regions of sinusoidal quantity.
Notes: 22

## Slide 9: Effective or Root Mean Square (RMS) Value review
The average value of a sinusoidal waveform is zero. So how does a sinusoidal voltage provide power or produce heat in a resistor for example. Hint: power is given by i2R or v2/R or vi
For the two cases shown, for same average power find the relationship between the dc and ac sources
Boylestad, Prentice Hall 2007

## Slide 10: Effective or Root Mean Square (RMS) Value review
We can equate the average (mean) power due to the ac source over a cycle (0 - 2p) to Pdc. Noting that the average value of the cos2wt is zero,
is called the effective value of the sinusoidal current

## Slide 11: Effective (rms) Values
The formula for power delivered by the ac supply at any time is:
The average power delivered by the ac source is just the first term, since the average value of a cosine wave is zero even though the wave may have twice the frequency of the original input current waveform.
Notes: 23

## Slide 12: Effective (rms) Values
The equivalent dc value is called the effective value of the sinusoidal quantity
or
  and
or
    Where: Im and Em are max (peak) values
Notes: 24

## Slide 13: Effective or Root Mean Square (RMS) Value review
The mathematical process involved (in order)
Squaring the waveform
taking the Mean (average)
taking the square Root
The above process can be applied to any periodic waveform to obtain the RMS value

## Slide 14: Effective or Root Mean Square (RMS) Value
Example 13.23 Boylestad (page 569)
Calculate the rms value of the voltage waveform in Fig. 13.62
Boylestad, Prentice Hall 2007

## Slide 15: Effective (rms) Values
Instrumentation
  A true rms meter will read the effective value of any waveform and is not limited to only sinusoidal waveforms.
  You should make sure that your meter is a true rms meter, by checking the manual, if waveforms other than purely sinusoidal are to be encountered.
Notes: 25

## Slide 16: Response of R, L and C
The response of the basic R, L, and C elements to a sinusoidal voltage and current will be examined with a special note of how frequency will affect the “opposing” characteristic of each element.
Phasor notation will then be introduced to establish a method of analysis.
Notes: 2

## Slide 17: The Derivative
To understand the response of the basic R, L, and C elements to a sinusoidal signal, you need to examine the concept of the derivative.
The derivative dx/dt is defined as the rate of change of x with respect to time. If x fails to change at a particular instant, dx = 0, and the derivative is zero.
For the sinusoidal waveform, dx/dt is zero only at the positive and negative peaks (wt = p/2 and 3p/2) since x fails to change at these instants of time.
Notes: 3

## Slide 19: The Derivative
The derivative dx/dt is actually the slope of the graph at any instant of time.
The greatest change in x will occur at the instants wt = 0, p, and 2p.
For various values of wt between these maxima and minima, the derivative will exist and will have values from the minimum to the maximum inclusive.
The derivative of a sine wave is a cosine wave; it has the same period and frequency as the original sinusoidal waveform.
Notes: 4

## Slide 21: Sinusoidal Response: Resistor
For a resistor the voltage and current are in phase and are related by Ohm’s law

## Slide 22
The voltage and current of a resistive element are in phase.

## Slide 23: Sinusoidal Response: Inductors
For an inductor the current lags the voltage by 90 degrees
XL = L is called the inductive reactance - unit 

## Slide 24: Sinusoidal Response: Waveforms
Inductor

## Slide 25: Sinusoidal Response: Capacitors
For a capacitor the current leads the voltage by 90 degrees
Xc = 1/C is called the capacitive reactance – unit 

## Slide 26: Sinusoidal Response: Waveforms
Capacitor

## Slide 27: Sinusoidal Response
The current through a 5 ohm resistor is i = 40sin(377t + 30°) A. Find the expression for voltage across it.

## Slide 28: Sinusoidal Response
The current through a 0.1H coil is i = 7sin(377t – 70°) A. Find the voltage across it.

## Slide 30: Capacitor Example

## Slide 32: More questions

## Slide 35: Low and High Frequency Response for Inductors
Inductors: XL = ωL
  At low frequencies, and especially DC, the reactance of a inductor is very low (zero for DC)
  Hence at very low frequencies, an inductor may be considered as a short circuit
  As input frequencies become very high, the reactance of an inductor approaches infinity
  Hence at very high frequencies, an inductor may be considered as an open circuit
Boylestad, Prentice Hall 2007

## Slide 36: Low and High Frequency Response for Capacitors
Capacitors: Xc = 1/ωC
  At low frequencies, and especially DC, the reactance of a capacitor is very high (infinite for DC)
  Hence at very low frequencies, a capacitor may be considered as an open circuit
  As input frequencies become very high, the reactance of a capacitor approaches 0Ω
  Hence at very high frequencies, a capacitor may be considered as a short circuit

## Slide 37: Average Power and Power Factor
Second term has a zero average value over a cycle and causes no average power
First term is independent of (a) time and is constant (b) whether v leads or lags i, and will be the Average Power or the Real Power
In general v = Vm sint and I = Im sin(t-)

## Slide 38: Average Power and Power Factor

Boylestad, Prentice Hall 2007

## Slide 39: Average Power and Power Factor
where V and I are rms values of the sinusoidal voltage and current respectively
The factor (cos ) which controls the average power flow is called the Power Factor.
For a resistor the Power Factor is unity
For an inductor or capacitor Power Factor is zero
Another way of finding the Power Factor is to use the expression

## Slide 40: Average Power and Power Factor
When the power factor is stated it is important to state whether it is leading or lagging in addition to its value (note that it lies between 0 and 1.0)

## Slide 41: Average Power and Power Factor
Vrms = Vpeak/sqrt(2)
Irms = Ipeak/sqrt(2)

## Slide 42: Average Power and Power Factor

## Slide 44: Power Factor Fp
Power Factor = Fp = cos 
The term leading or lagging is often written in conjunction with the power factor.
They are defined by the current through the load.
If the current lead the voltage then its a leading power factor
If the current lags the voltage then its a lagging power factor
Capacitive circuits have leading power factors, while Inductive circuits have lagging power factors

## Slide 45: Example Power factor

## Slide 47: Complex Numbers
As an essential tool complex numbers will be used in solving ac circuits
Rectangular form Z = a + j b
where ‘j’ is an operator which turns the real number ‘b’ by 90° in the anti-clockwise direction on the complex plane
Polar form Z = Z /°
Addition is convenient in rectangular form
Division/multiplication is convenient in polar form
a
jb

## Slide 48: Complex Numbers
Defining the rectangular form.

## Slide 49: Polar form
Defining the polar form.
Demonstrating the effect of a negative sign on the polar form.

## Slide 51: Complex Conjugate

## Slide 52: Conversion Between Forms

## Slide 53: Complex Numbers

## Slide 54: Complex Numbers

## Slide 55: Maths Operations

## Slide 57: Polar form operations

## Slide 58: Phasors and Phasor Diagrams
Often addition/subtraction of sinusoidal voltages and currents is required in ac circuit analysis.
For example consider the addition of two sinusoidal signals
v1 = Vm1 sin (wt +) and v2 = Vm2 sin wt
We can add the two waveforms on a point-by-point basis as shown (a tedious process!!) to obtain vT.
Boylestad

## Slide 59: Phasors and Phasor Diagrams
However it is very convenient to represent the two sinusoidal waveforms v1 = Vm1 sin (wt +) and v2 = Vm2 sin wt as vectors and then add the vectors. These vectors are called phasors.

V2=Vm2/0
VmT
Phasor diagram of V1, V2 and VT
Note the phasors with underscore – in the book shown in bold
V1=Vm1/

## Slide 60: Phasors and Phasor Diagrams
Phasors are characterised by a magnitude and a phase angle
It is common to represent the magnitude of a phasor as an rms quantity rather than a peak value
They represent a snap shots of the rotating vectors at t = 0
They do not carry information about the frequency

V2=V2/0°
VT
V1=V1/°

## Slide 61: Phasor Addition